## Slide 1
Regular camera mode
Display mode
Exposure: 1039 ms
Error : +67
A7 0A FF FF 01 00 01 03
Clock/1 REG:FFFF
/Camera/0000001.bmp
No delay 82FP
HDR mode OFF 5L
Main ON/OFF switch
Display switch
(saves battery during timelapses)
Activates dithering
Locks exposure
(border becomes green)
Take a picture !
Activates HDR mode ± 1EV
(requires a tripod)
Cycles between:
Regular camera mode
Burst mode
Timelapse 1 s delay
Timelapse 30 s delay
Timelapse 60 s delay
Slit scan mode infinite
Slit scan mode 128 pixels
Motion sensor mode
Cycle fast to change between borders (7 possible + no border)
REBOOT
TIMELAPSE
LOCK_EXP
DITHER
HDR
PUSH
DISPLAY
MAIN
Mode chosen
What the DashBoy does
/general informations
How far from perfect exposure
Actual exposure time
Actual exposure area
Current camera registers
Sensor clock divider if night mode
Current exposure registers
Type of sensor
Exposure strategy (see code)
Current file recorded
HDR mode
active or not
Delay to the next image if any
Green when sensor is being exposed
Access to SD
/error
/acknowledge